| PCM Connector C1 (Blue) |
| --- |
| Connector Part Information | PCM Connector C1 92231110 80-Way Micro-Pack 100W Series Sealed (BU) |
| Pin | Wire Color | Circuit No. | Function |
| 1 | BK/RD | 450 | Ground |
| 2 | L-BU/WH | 2867 | 12-Volt Reference - CKP Sensor |
| 3 | PU | 1746 | Fuel Injector 3 Control |
| 4 | GN | 1745 | Fuel Injector 2 Control |
| 5-6 | -- | -- | Not Used |
| 7 | BU/YE | 596 | 5-Volt Reference - EOP Sensor |
| 8 | GY | 2701 | 5-Volt Reference - TP Sensor |
| 9-10 | -- | -- | Not Used |
| 11 | L-BU | 1876 | KS 2 Signal |
| 12 | L-BU | 573 | CKP Sensor Signal |
| 13-16 | -- | -- | Not Used |
| 17 | YE | 1225 | Transmission Fluid Pressure Switch Signal B |
| 18 | GY | 1226 | Transmission Fluid Pressure Switch Signal C |
| 19 | OG | 300 | Ignition 3 Voltage |
| 20 | OG | 740 | Battery Positive Voltage |
| 21 | L-BU/BK | 574 | Low Reference - CKP Sensor |
| 22 | -- | -- | Not Used |
| 23 | BK | 2759 | Low Reference - FTP Sensor and Fuel Level Sensor |
| 24 | BK/RD | 450 | Ground |
| 25 | TN | 1671 | HO2S Low Signal Bank 2 Sensor 2 |
| 26 | GY/BK | 1667 | HO2S Low Signal Bank 2 Sensor 1 |
| 27 | BK/RD | 450 | Ground |
| 28 | TN/WH | 1669 | HO2S Low Signal Bank 1 Sensor 2 |
| 29 | BU/BK | 1664 | HO2S Low Signal Bank 1 Sensor 1 |
| 30 | GN | 68 | Engine Coolant Level Signal |
| 31 | -- | -- | Not Used |
| 32 | BU/WH | 771 | Transmission Range Switch Signal A |
| 33 | BN | 86 | Cruise Control Release Signal |
| 34 | WH | 776 | Transmission Range Switch Signal P |
| 35 | -- | -- | Not Used |
| 36 | BU | 1744 | Fuel Injector 1 Control |
| 37 | YE | 846 | Fuel Injector 6 Control |
| 38-39 | -- | -- | Not Used |
| 40 | BK/RD | 450 | Ground |
| 41-42 | -- | -- | Not Used |
| 43 | PK/BK | 877 | Fuel Injector 7 Control |
| 44 | BN/YE | 844 | Fuel Injector 4 Control |
| 45 | PU/WH | 2700 | 5-Volt Reference - A/C Refrigerant Pressure Sensor |
| 46 | GY | 2709 | 5-Volt Reference - FTP Sensor |
| 47 | -- | -- | Not Used |
| 48 | PU/WH | 2704 | 5-Volt Reference - MAP Sensor |
| 49-50 | -- | -- | Not Used |
| 51 | BU | 496 | KS 1 Signal |
| 52 | -- | -- | Not Used |
| 53 | BK/WH | 2762 | Low Reference - TFT Sensor |
| 54 | BK | 469 | Low Reference - MAP Sensor |
| 55-56 | -- | -- | Not Used |
| 57 | OG | 740 | Battery Positive Voltage |
| 58 | YE | 1045 | RFA Class 2 Serial Data |
| 59 | -- | -- | Not Used |
| 60 | BK/YE | 2752 | Low Reference - TP Sensor |
| 61 | RD/WH | 632 | Low Reference - CMP Sensor |
| 62 | -- | -- | Not Used |
| 63 | GN | 470 | Low Reference - EOP Sensor |
| 64 | BK/RD | 450 | Ground |
| 65 | PU/BK | 1670 | HO2S High Signal Bank 2 Sensor 2 |
| 66 | GY | 1666 | HO2S High Signal Bank 2 Sensor 1 |
| 67 | BK/RD | 450 | Ground |
| 68 | PU/WH | 1668 | HO2S High Signal Bank 1 Sensor 2 |
| 69 | PU | 1665 | HO2S High Signal Bank 1 Sensor 1 |
| 70-71 | -- | -- | Not Used |
| 72 | YE/RD | 772 | Transmission Range Switch Signal B |
| 73 | BN | 633 | Camshaft Position Signal |
| 74 | YE | 410 | ECT Sensor Signal |
| 75 | -- | -- | Not Used |
| 76 | GY | 845 | Fuel Injector 5 Control |
| 77 | L-GN | 878 | Fuel Injector 8 Control |
| 78 | -- | -- | Not Used |
| 79 | GN/WH or GY | 898 or 587 | Shift Solenoid Valve 3 High Control - Skip/Shift Solenoid Control |
| 80 | GY/BK | 2761 | Low Reference - ECT Sensor |