| PCM Connector C2 (Green) |
| --- |
| Connector Part Information | PCM Connector C2 92231110 80-Way Micro-Pack 100W Series Sealed (GN) |
| Pin | Wire Color | Circuit No. | Function |
| 1 | BK/RD | 450 | Ground |
| 2 | BN | 418 | TCC PWM Solenoid Valve Control |
| 3-5 | -- | -- | Not Used |
| 6 | RD | 1228 | PC Solenoid Valve High Control Sol.A |
| 7 | -- | -- | Not Used |
| 8 | GY/BU | 1229 | PC Solenoid Valve Low Control Sol.A |
| 9 | GN/WH | 465 | Fuel Pump Relay Control Primary |
| 10 | BN | 121 | Engine Speed Signal - Tachometer |
| 11 | -- | -- | Not Used |
| 12 | GY/BK | 1687 | Ignition Retard Signal, from EBCM |
| 13 | -- | -- | Not Used |
| 14 | GN/BK | 380 | A/C Refrigerant Pressure Sensor Signal |
| 15-17 | -- | -- | Not Used |
| 18 | GN | 59 | A/C Compressor Clutch Supply Voltage |
| 19 | -- | -- | Not Used |
| 20 | TN | 1231 | AT ISS Low Signal |
| 21 | BU/WH | 1230 | AT ISS High Signal |
| 22-23 | -- | -- | Not Used |
| 24 | BU | 411 | TP Sensor Signal |
| 25 | BN | 472 | IAT Sensor Signal |
| 26 | WH | 2121 | IC 1 Control |
| 27 | YE | 2127 | IC 7 Control |
| 28 | L-GN | 2126 | IC 6 Control |
| 29 | WH | 2124 | IC 4 Control |
| 30 | -- | -- | Not Used |
| 31 | BN/WH | 492 | MAF Sensor Signal |
| 32 | L-GN | 432 | MAP Sensor Signal |
| 33 | BU/WH | 473 | High Speed Cooling Fan Relay Control |
| 34 | GN/YE | 428 | EVAP Canister Purge Solenoid Control |
| 35-38 | -- | -- | Not Used |
| 39 | WH/BK | 631 | 12-Volt Reference - CMP Sensor |
| 40 | BK/RD | 450 | Ground |
| 41 | -- | -- | Not Used |
| 42 | GY/RD | 422 | TCC Solenoid Valve Control |
| 43 | L-GN/BK | 459 | A/C Clutch Relay Control |
| 44 | YE | 1652 | Reverse Lock Out Solenoid Control |
| 45 | WH | 1310 | EVAP Canister Vent Solenoid Control |
| 46 | BN/WH | 419 | MIL Control |
| 47 | YE/BK | 1223 | 2-3 Shift Solenoid Valve Control |
| 48 | L-GN | 1222 | 1-2 Shift Solenoid Valve Control |
| 49 | -- | -- | Not Used |
| 50 | PU/WH | 5197 | VSS Signal |
| 51 | YE/BK | 1227 | TFT Sensor Signal |
| 52 | L-BU | 1150 | HO2S Bank 1 Sensor 2 Heater Control |
| 53 | RD/WH | 1350 | HO2S Bank 2 Sensor 2 Heater Control |
| 54 | PU | 30 | Fuel Level Sensor Signal |
| 55-56 | -- | -- | Not Used |
| 57 | GN/OG | 5514 | Low Reference - IAT Sensor and A/C Refrigerant Pressure Sensor |
| 58 | BN/WH | 331 | Engine Oil Pressure (EOP) Sensor Signal |
| 59 | -- | -- | Not Used |
| 60 | BN | 2129 | Low Reference - Ignition Coils Bank 1 |
| 61 | PU | 2130 | Low Reference - Ignition Coils Bank 2 |
| 62 | GY | 773 | Transmission Range Switch Signal C |
| 63 | BN/YE | 1224 | Transmission Fluid Pressure Switch Signal A |
| 64 | D-GN | 890 | Fuel Tank Pressure (FTP) Sensor Signal |
| 65 | -- | -- | Not Used |
| 66 | L-BU | 2128 | IC 8 Control |
| 67 | YE/BK | 2122 | IC 2 Control |
| 68 | GN | 2125 | IC 5 Control |
| 69 | BU | 2123 | IC 3 Control |
| 70-71 | -- | -- | Not Used |
| 72 | BK/WH | 1050 | HO2S Bank 1 Sensor 1 Heater Control |
| 73 | -- | -- | Not Used |
| 74 | L-GN/RD | 1250 | HO2S Bank 2 Sensor 1 Heater Control |
| 75 | -- | -- | Not Used |
| 76 | L-GN/WH | 1749 | IAC Coil B High Control |
| 77 | L-GN/BK | 444 | IAC Coil B Low Control |
| 78 | L-BU/BK | 1748 | IAC Coil A Low Control |
| 79 | L-BU | 1747 | IAC Coil A High Control |
| 80 | -- | -- | Not Used |