Black 14 pin connector.  Not labled a-n, just identify order by wire color/placement.

A 	blu/blk pin 13 cruise engage			Depends

B	wht  Power steering pump pressure sensor	No

C	pnk canister evap vent			Depends

D	grn  pin 50 VSS out				Depends

E 	ppl pin 33 TCC Break switch			If using 4l60e/ 80e yes

F	brn/wht MIL control				Yes

G	Grn pin 58 serial data				Yes

H 	tan/wht oil pressure				Depends

I	wht pin 10 Tachometer 			Depends

J	brn Power steering pump pressure sensor	No

K 	yel VATS					No unless using BCM

L	brn 4wd low					No

M   	grn A/C recirc. 				No

N   	grn/blk to fuse center 				Me no, but you ?????????

Blue 12 pin plug

A

B

C 	Gry	pin 45 evap vent 			Depends

D	grn	pin 64 fuel signal control		Depends

E	yel/blk	pin 49 VSS out			Depends

F	wht	pin 45 EVAP vent 			Depends

G	orng/blk  Pin 80 Blue connector No idea what it does??????????????

H

J	blk 	pin 53 Blue ????????????????????????

K	ppl	pin 54 Fuel level 			Depends

L

M

2 Pin black connector is fo 4WD low range 		Not used

Large Black plug for fuse box.  Not labled just follow diagram to find wires

Pnk		Injection 2&4			Yes

blk 		ground 			Yes

pnk 		coils odd			Yes

pnk 		ignition 1			Yes

ppl 		Starter				Depends

yel 		PRND switch			No

pnk 		Injection 1&3			Yes

pnk		injection 5&7			Yes

ppl/wht	PRND 				No

grn		PRND				No

pnk		PRND				No

Orng 		Battery				Yes

pnk		Front o2			Yes

pnk 		Rear o2 			Depends

dk grn/wht	Fuel pump relay		Yes

pnk 		evap purge			Depends

pnk 		injectors 6&8			Yes

blk 		Ground			Yes

pnk 		coils even			Yes

blk/wht 	ground				Yes

LT Blue	A/C 				Depends

pnk 		MAF				Yes

drk blu		A/C recirc.			No

Grn 		A/C compressor		Depends

LT grn 	PRND  			No

grn/blk 	to blk connector		No/Depends

pnk 		evap vent			Depends

pnk 		Ignition 2 pin 75 		Yes