| 2010 Hydra-Matic 6T75 ( MY9 ) FWD | 06/05/2009 |
| --- | --- |
| Type: | Six speed front-wheel-drive (FWD), electronically controlled, automatic overdrive transaxle with an electronically controlled torque converter clutch. 2 Wheel Drive model |
| Engine range: | 3.6L - 4.6L |
| Maximum engine torque: | 301 lb-ft (406 Nm) |
| Maximum gearbox torque: | 380 lb-ft (515Nm) all gears |
| Gear ratios: | MY9 |
| First | 4.484 |
| Second | 2.872 |
| Third: | 1.842 |
| Fourth: | 1.414 |
| Fifth | 1 |
| Sixth | 0.742 |
| Reverse: | 2.882 |
| Final Drive Ratio: | 3.16 |
| Maximum input speed: | Rev 5000 rpm |
|  | 1-2 7000 rpm |
|  | 2-3 7000 rpm |
|  | 3-4 7000 rpm |
|  | 4-5 6500 rpm |
|  | 5-6 5798 rpm |
| Maximum validated gross vehicle weight: | 2930 kg (6460 lbs) |
| Shifter Posistions: | P, R, N, D, M, (DSC+/-) & L (MU/MD) |
| Case material: | die cast aluminum |
| Shift pattern: | 6 Variable Bleed Solenoids |
| Shift quality: | 6 Variable Bleed Solenoids |
| Torque converter clutch: | Variable Bleed Solenoid |
| Converter size: | 246mm (reference) (diameter of torque converter turbine) |
| Fluid type: | DEXRON® VI; 9986153; Spec:GMN10060 |
| Transmission weight: | wet: 104.4 - 104.7 kg |
| Fluid capacity (approximate): | 9.0L (9.5 qt) |
| Bottom pan removal: | NA |
| Pressure taps available: | line pressure |
| Transfer design: | three-axis design |
| Assembly sites: | Warren, Mich.; Ramos Arizpe, Mexico |
| RPO Differences: | MY9 - 2wd |
|  | MH6 - Awd |
| Applications: | GMC Acadia |
|  | Buick Enclave |
|  | Chevrolet Traverse |