| 2006 "LS4" 5.3L V8 ( LS4 ) |  |
| --- | --- |
| Type: | 5.3L Gen IV V8 Small Block |
| Displacement: | 5328cc (325 ci) |
| Compression ratio: | 10:1 |
| Valve configuration: | overhead valves (2 valves per cylinder) |
| Assembly site: | St. Catharines, Ontario, Canada |
| Valve lifters: | hydraulic roller |
| Firing order: | 1 - 8 - 7 - 2 - 6 - 5 - 4 - 3 |
| Bore x stroke: | 96.0 x 92.0 mm |
| Fuel system: | sequential fuel injection |
| Fuel Type: | Premium Fuel recommended |
| Ignition System: | Coil-near-plug |
| Application: | Horsepower: hp ( kw ) |
| Chevrolet Impala SS | 303 hp (226 kw) @ 5600 rpm |
| Chevrolet Monte Carlo SS |  |
| Pontiac Grand Prix GXP |  |
| Application: | Torque: lb-ft. ( Nm ) |
| Chevrolet Impala SS | 323 lb-ft (438 Nm ) @ 4400 rpm |
| Chevrolet Monte Carlo SS |  |
| Pontiac Grand Prix GXP |  |
| Fuel shut off: | 6100 rpm |
| Emissions controls: | catalytic converter |
|  | three-way catalyst |
|  | positive crankcase ventilation |
| MATERIALS |  |
| Block: | cast aluminum |
| Cylinder head: | cast aluminum |
| Intake manifold: | composite |
| Exhaust manifold: | cast nodular iron |
| Main bearing caps: | powder metal |
| Crankshaft: | cast nodular iron with undercut and rolled fillets |
| Camshaft: | hollow steel |
| Connecting rods: | powder metal |
| Additional features: | extended life spark plugs |
|  | extended life coolant |
|  | oil level sensor |
|  | Oil Life System |
|  | Active Fuel Management |