NOTE: Emission compliance is your responsibility! This document is for use on OFF-ROAD USE VEHICLES ONLY. NOT FOR STREET DRIVEN VEHICLES.

To begin the process of converting the 1998 F harness to the 1999-2002 F harness start with C1 RED connector. Take notice, the 1998 PCM C1 is RED and the C2 connector is BLUE. The opposite is true for the 1999 –2002 PCM. C1 is BLUE and C2 is RED. If you are performing this “in car,” disconnect the battery to avoid arc welding. Remove the Red and Blue covers and label the aluminum connector housings using a permanent marker with the colors red and blue. Some terminal locations in the connector will need to be perforated with a small sharp pick to allow the terminal to slide into its new location.

The numbered instructions have the color of the connector noted “Red” or “Blue.” The 1998 location & wire color (in Caps) are next then followed by “TO” where it goes on the later model harness. Some circuits will be deleted if present. EGR circuits will be shown for 1999/2000 conversions. The EGR wires can be installed in 2001-2002 applications if desired.  Some circuits will fit best if extended. Label them and extend them after swapping is finished. Use the “Check Auto/Manual” Excel file to verify the swap. The colors and circuits reflect the 1998 color code that is sometimes different from the later models.

- Red C1-3 WHT TO Red C2-45

- Red C1-45 DK GRN/WHT TO Red C2-34

- Red C1-34 WHT (auto) or GRAY (manual) TO Blue C1-79

- Red C1-4 BRN/WHT TO Blue C1-73

- Red C1-7 YEL TO Red C2-21

- Red C1-21 PPL TO Red C2-57

- Red C1-57 DK GRN/WHT TO Red C2-29

- Blue C2-21 BLK TO Blue C1-40

- Red C1-72 BLK TO Red C2-1

- Red C1-76 BLK TO Red C2-40

- Red C1-40 YEL/BLK TO Red C2-47; for manual trans discard WHT (Note 1)

- Red C1-47 DK GRN/WHT TO Red C2-17

- Blue C2-47 PPL/WHT TO Blue C1-69

- Blue C2-69 DK BLU TO Blue C1-51

- Blue C2-62 LT GRN TO Blue C1-2           Recommended to Extend

- Blue C2-2 TAN/WHT TO Blue C1-28

- Blue C2-28 DK BLU TO Red C2-33          Recommended to Extend

- Red C1-33 BLK TO Blue C1-36

- Blue C2-36 LT BLU/WHT TO Red C2-8

- Blue C2-1 TAN TO Blue C1-25

- Blue C2-25 BRN TO Blue C1-80

- Red C1-11 DK BLU TO Red C2-30

- Red C1-30 GRY/BLK TO Red C2-53, if not present, skip this step.

- Red C1-53 RED TO Red C2-27

- Red C1-27 RED/BLK TO Blue C1-43

- Blue C2-43 GRY TO Blue C1-8

- Blue C2-8 TAN TO Red C2-25

- Red C1-25 PNK TO Red C2-63

- Red C1-63 BLK TO Red C2-57 SPLICE? Or Blue C1-63

- Blue C2-30 BRN TO Red C2-36                 Recommended to Extend

- Red C1-36 DK BLU TO Red C2-38……………TEST FIRST! 99-02 PCM’S

- Red C1-12 LT BLU/BLK TO Blue C1-44

- Red C1-44 YEL TO Blue C1-12

- Blue C2-12 DK BLU TO Red C2-24

- Red C1-24 BLK/WHT If present discard it and Blue C2-24

- Red C1-13 RED/WHT TO Red C2-67

- Blue C2-67 GRY TO Blue C1-46

- Blue C2-46 PPL TO Blue C1-66

- Blue C2-66 GRY TO Blue C1-45

- Red C1-14 DK GRN TO Red C2-18

- Red C1-18 YEL/BLK TO Blue C1-37

- Blue C2-37 DK GRN/WHT TO Red C2-9       Recommended to Extend

- Blue C2-3 TAN delete

- Red C1-9 PNK/BLK TO Blue C1-3

- Red C1-15 BLK/WHT TO Blue C1-76

- Blue C2-76 BRN TO Blue C1-70

- Blue C2-70 PNK/BLK TO Blue C1-61

- Blue C2-61 ORN TO Blue C1-57

- Blue C2-57 LT GRN/WHT TO Red C2-76

- Red C1-37 BRN/WHT TO Red C2-46

- Red C1-22 DK BLUE TO Blue C1-17

- Red C1-23 LT GRN/BLK TO Blue C1-4

- Blue C2-4 RED TO Red C2-39

- Red C1-39 DK GRN/WHT TO Red C2-43

- Red C1-43 DK GRN TO Blue C1-42

- Blue C2-42 PPL/WHT TO Blue C1-68

- Blue C2-68 LT BLU TO Blue C1-11

- Red C1-31 DK BLU/WHT TO Blue C1-77

- Red C1-77 PPL TO Blue C1-33

- Blue C2-33 BRN TO Red C2-2

- Blue C2-38 LT BLU TO Red C2-7 for 99-00 w/EGR. 01/02 Discard

- Blue C2-7 RED/BLK TO Red C2-14                 Recommended to Extend

- Blue C2-14 ORG/BLK TO Blue C1-53

- Red C1-32 ORG/BLK TO Blue C1-34

- Blue C2-34 GRY TO Red C2-41 for 99/00 w/EGR 01/02 discard

- Red C1-35 LT GRN TO Red C2-48

- Red C1-48 YEL TO Red C2-31

- Blue C2-48 LT GRN TO Red C2-32

- Blue C2-32 TAN/BLK TO Red C2-42

- Red C1-42 LT GRN TO Red C2-44 manual transmission only.

- Blue C2-41 PPL TO Blue C1-65

- Blue C2-65 GRY TO Blue C1-47

- Blue C2-31 PPL TO Red C2-4                             Recommended to Extend

- Blue C2-39 RED/BLK TO Red C2-6

- Blue C2-6 TAN/WHT TO Blue C1-29

- Red C1-49 PPL TO Red C2-26

- Blue C2-26 ORN/BLK TO Blue C1-54

- Blue C2-54 LT GRN/BLK TO Red C2-77

- Red C1-54 LT BLU/WHT TO Red C2-28

- Red C1-52 PPL/WHT TO Red C2-66

- Red C1-55 DK GRN/WHT TO Red C2-50

- Red C1-56 DK GRN TO Red C2-68

- Red C1-58 LT BLU TO Red C2-69

- Red C1-59 BRN/WHT TO Red C2-61

- Red C1-61 RED TO Blue C1-18

- Red C1-62 BLK TO Blue C1-41

- Red C1-71 PPL TO Red C2-20

- Red C1-75 GRY TO Blue C1-23

- Blue C2-23 BLK TO Blue C1-60

- Blue C2-60 BLK TO Blue C1-1

- Blue C2-5 TAN TO Blue C1-26

- Blue C2-9 BRN TO Blue C1-55

- Blue C2-55 LT BLU/BLK TO Red C2-78

- Blue C2-10 PPL TO Red C2-54

- Blue C2-13 YEL/BLK TO Red C2-51

- Blue C2-22 YEL/BLK TO Blue C1-21

- Blue C2-35 WHT TO Red C2-10

- Blue C2-49 YEL TO Blue C1-74

- Blue C2-52 DK GRN TO Red C2-64

- Blue C2-64 GRY TO Blue C1-48

- Blue C2-56 LT BLU/WHT TO Red C2-79

- RED C1-41 BRN/WHT delete, was for low oil light.

NOTE: Red C1-60 BRN, Blue C2-19 PNK, C2-58 PPL and C2-20 ORN remain in the same locations.

The low oil light will not work in the dash of the 1998 car. It can be wired in elsewhere if desired. See omitted wire from RED C1-41 BRN/WHT.

Traction control UART data is not supported in the later PCM.

Additional notes for manuals:

- The skip shift light will not function with the 1998 cluster. It can be wired in elsewhere if desired. See omitted wire from Red C1-40 WHT.

- The clutch pedal position sensor needs to be wired in. If not code P0704 will set.

Cruise Control is not affected by the 1998 PCM.  The cruise will work as normal.

Copyright ChipsByAl LLC 2007